## Slide 1: ANVIKSHA
8 - Bit Central Processing Unit

## Slide 2: STEP 1: Power Supply (FOUNDATION)
What to do:
Set up 5V regulated supply
7805 + capacitors OR USB 5V
Connect +5V and GND rails
Add 0.1µF capacitor near every IC
Add a power LED
Test:
✔ Measure 5V using multimeter
✔ No IC should heat up
Don’t move forward if power isn’t stable

## Slide 3: STEP 2: Clock Circuit (HEARTBEAT)
What to do:
Build 555 timer astable
Add potentiometer for speed control
Add push-button single-step clock
Clock LED output
Test:
✔ LED blinks slow/fast
✔ Push button → 1 pulse = 1 blink
🟢 You must be able to pause and single-step

## Slide 4: STEP 3: 8-BIT DATA BUS
What to do:
Create 8 parallel bus lines
Label D0–D7
Add LEDs + resistors (optional but recommended)
Use 74LS245 for bus control
Test:
✔ Drive bus with switches
✔ LEDs reflect correct value
⚠️ Only ONE output may drive bus at a time

## Slide 5: STEP 4: Register A (FIRST STORAGE)
What to do:
Use 74LS173 / 74HC173
Inputs ← data bus
Output → bus (via tri-state)
Add LOAD and ENABLE signals
Test:
✔ Put value on bus
✔ LOAD → value stored
✔ ENABLE → value appears on bus
This proves your CPU can remember data

## Slide 6: STEP 6: ALU (MATH ENGINE)
What to do:
Build adder (74LS181 ×2 or 74LS283)
Inputs from Register A & B
Output → data bus
Capture Carry & Zero flags
Test:
✔ 3 + 4 → 7
✔ Carry LED lights correctly
This is the soul of your CPU

## Slide 7: STEP 7: Program Counter (PC)
What to do:
Use 74LS161
Increment every instruction
Output → address bus
Add RESET & LOAD (jump)
Test:
✔ Counts 0 → 255
✔ Reset works

## Slide 8: STEP 8: Instruction Register (IR)
What to do:
Load instruction from memory
Upper 4 bits → opcode
Lower 4 bits → operand
Test:
✔ Instruction stays stable while executing

## Slide 9: STEP 9: Control Unit (BRAIN)
What to do:
Use EEPROM (AT28C16)
Address = opcode + step counter
Output = control signals
Generate:
  Register load
  ALU select
  PC increment
  Memory read
Test:
✔ Correct signals per clock step
⚠️ This step needs patience

## Slide 10: STEP 10: Memory (PROGRAM STORAGE)
What to do:
ROM → instructions
RAM → data
Address from PC
Data → bus
Test:
✔ CPU fetches correct instruction

## Slide 11: STEP 11: Output Register
What to do:
Capture bus value
Display on LEDs
Test:
✔ OUT instruction works